QUESTION 1:

Please provide the EXCEL spreadsheets showing the cost allocation (SCG 2013TCAP Cost Allocation) and rate design (2013TCAP SCG RD Model) results using all the methods in your current proposal (system integration of transmission facilities) but assume the $31.5 million of SDG&E transmission costs are considered to be local transmission facilities.

RESPONSE 1:

SoCalGas/SDG&E assumed for this response that the general BTS rate design methodology was held intact.  Since SDG&E’s transmission costs were assumed to be all local, the BTS rate was made up entirely of SoCalGas’ $116.1 million in BB costs.  Local Transmission costs, now $81.9 million instead of $50.4 million as proposed, still went through the system-integration process.  The model updates that had to be made were (see yellow highlighted tabs/cells):

- SDG&E Cost Allocation

  - Change Transmission from 100% BB to 100% LT

- SoCalGas Rate Design

  - On “SI&BTS” tab, change target BB Rev Req from $147.5 million to $116.1 million

  - Reran scenarios on tab “TCAP Rate Summary”

  - Tabs “Bonnett Testimony Tables” and “Lenart Testimony Tables” automatically updated from new scenario data on “TCAP Rate Summary” tab

QUESTION 2:

Please provide the EXCEL spreadsheets showing the cost allocation (SCG 2013TCAP Cost Allocation) and rate design (2013TCAP SCG RD Model) results assuming no system integration of transmission costs.

RESPONSE 2:

For this response, SoCalGas/SDG&E assumed that all transmission costs were allocated to end-use transportation rates, and there was no BTS rate.  However, Sempra-wide rates (e.g. TLS) maintained their structure, which averages costs, including transmission costs, between the two utilities.  In order to present this case, the model updates made were (see yellow highlighted tabs/cells):

- SDG&E Cost Allocation

  - Change Transmission from 100% BB to 100% LT

- SDG&E Rate Design:

  - “Cost Alloc,” “NCCI-Detail,” and “EG-Detail” tabs updated to remove System Integration calculations, such that “Total Margin Allocation pre-SI, pre-BTS Unbundle w/FFU” equals “Total Margin Allocation post-SI, post-BTS Unbundle, w/ FFU”

- SoCalGas Rate Design:

  - “SI&BTS” tab, all inputs zeroed out, essentially nullifying System Integration

  - “Cost Alloc,” “NCCI-Detail,” and “EG-Detail” tabs updated to remove System Integration calculations, such that “Total Margin Allocation pre-SI, pre-BTS Unbundle w/FFU” equals “Total Margin Allocation post-SI, post-BTS Unbundle, w/ FFU”

  - Reran scenarios on tab “TCAP Rate Summary”

  - Tabs “Bonnett Testimony Tables” and “Lenart Testimony Tables” automatically updated from new scenario data on “TCAP Rate Summary” tab

QUESTION 3:

Please provide the EXCEL spreadsheets showing the cost allocation (SCG 2013TCAP Cost Allocation) and rate design (2013TCAP SCG RD Model) results assuming a) the SDG&E transmission costs are considered to be local transmission recovered only from SDG&E customers, b) SoCalGas local transmission costs are recovered from SoCalGas customers, and c) the SoCalGas backbone transmission costs are allocated based on a system integration approach to both SoCalGas and SDG&E customers.

RESPONSE 3:

For this response, SoCalGas/SDG&E assumed that all local transmission costs were allocated directly to end-use transportation rates without any System Integration calculations, but the BTS rate was maintained for Backbone costs.  Since SDG&E’s transmission costs were assumed to be all local, the BTS rate was made up entirely of SoCalGas’ $116.1 million in BTS costs.  The model updates made were (see yellow highlighted tabs/cells):

- SDG&E Cost Allocation

  - Change Transmission from 100% BB to 100% LT

- SDG&E Rate Design:

  - “Cost Alloc,” “NCCI-Detail,” and “EG-Detail” tabs updated to remove Local Transmission System Integration calculations

- SoCalGas Rate Design:

  - “SI&BTS” tab, change target BB Rev Req from $147.5 million to $116.1 million and zeroed out Local Transmission inputs, essentially nullifying System Integration of LT

  - “Cost Alloc,” “NCCI-Detail,” and “EG-Detail” tabs updated to remove Local Transmission System Integration calculations

  - Reran scenarios on tab “TCAP Rate Summary” Tabs “Bonnett Testimony Tables” and “Lenart Testimony Tables” automatically updated from new scenario data on “TCAP Rate Summary” tab

QUESTION 4:

In response to a Division of Ratepayer Advocates’ Data Request, (request and response reproduced in blue below), SoCalGas/SDG&E stated, “some segments with a calculated hoop stress of less than 20% of SMYS are identified as transmission in the database.  As will be explained in our forthcoming Supplemental Testimony, these segments were identified as transmission during the population of the database.” Does SoCalGas/SDG&E consider the “criteria of “operates at a hoop stress of 20 percent or more of SMYS;” to apply to both backbone transmission and local transmission?

QUESTION DRA-DAO-TCAP-PSEP-33-01:

In the data extract provided by Sempra in response to DRA-16, Q.6, there are approximately 15 miles of pipelines that operated below 20% SMYS, ranging from 0% to 19% SMYS.  Please provide the following information regarding Sempra’s response to DRA-16, Q.6:

(a) Please confirm that all the segments of these lines meet the definition of a transmission line using 49 C.F.R. Part 192, § 192.3   Definitions:

Transmission line means a pipeline, other than a gathering line, that: (1) Transports gas from a gathering line or storage facility to a distribution center, storage facility, or large volume customer that is not down-stream from a distribution center; (2) operates at a hoop stress of 20 percent or more of SMYS; or (3) transports gas within a storage field.

- For each segment/line, please identify the criteria used to define it as a transmission line.  Please provide this information in a searchable Excel spreadsheet.

RESPONSE DRA-DAO-TCAP-PSEP-33-01:

- The spreadsheet provided in response to DRA-16-6 includes some distribution main as defined in 49 CFR 192.  On the revised version of the DRA-16-6 extract a column indicating if the segment is classified as Distribution or Transmission was added.  In some instances a pipeline will have segments that operate below 20% SMYS and above 20%SMYS, however the data collection was performed by line number to maintain continuity.  SoCalGas and SDG&E plan to serve supplemental testimony in this proceeding to explain the inclusion of some small distribution segments within the scope of Phase 1 of the proposed PSEP.

Generally, the criteria of “operates at a hoop stress of 20 percent or more of SMYS;” is used since facilities outside of the storage fields are considered as operating downstream of distribution center.  However, some segments with a calculated hoop

stress of less than 20% of SMYS are identified as transmission in the database.  As will be explained in our forthcoming Supplemental Testimony, these segments were identified as transmission during the population of the database.

RESPONSE 4:

Yes, the hoop stress criteria and other criteria included in 49 CFR §192.3 for transmission pipeline applies to SoCalGas pipelines that are jurisdictional to 49 CFR Part 192, including backbone and local transmission.

CFR 49 Part 192 defines the term “transmission line” for the application of the minimum safety requirements for pipeline facilities.  This definition includes a threshold for the stress level of the pipeline.  This definition is separate and independent from the pipeline categorizations of backbone transmission, local transmission, and distribution that are used for rate making.  Backbone and local transmission as well as distribution system pipe include pipeline or pipeline segments that meet the CFR 49 Part 192 definition of Transmission, and these three systems also include pipeline or pipeline segments that are not defined as transmission per CFR 49 Part 192.