Caution

Power to this building is also supplied

from the Following sources WITH

DISCONNECTS LOCATED as shown:

# Text boxes

THIS IS A SAMPLE OF THE PLAQUE OR DIRECTORY REQUIRED WHEN THERE IS ANY ALTERNATE SOURCE OF POWER CONNECTED TO THE PREMISES WIRING SYSTEM.  THE EXAMPLE BELOW SPECIFIES PHOTOVOLTAIC OR WIND GENERATION.  MODIFY AS REQUIRED FOR THE TYPE OF GENERATING FACILITY TO BE INSTALLED.

¾”

¼”

# X

# X

# X

# X

# X

# X

Wind Turbine or solar photovoltaic array remote location per zoning requirements

Utility Service point

ALTERNATE POWER

SOURCE AC DISCONNECT

For utility operation

1/8”

THE PLAQUE OR DIRECTORY SHALL BE METAL OR PLASTIC, WITH ENGRAVED OR MACHINE

PRINTED LETTERS, OR ELECTRO-PHOTO PLATING, IN A CONTRASTING COLOR TO THE PLAQUE,

AND SHALL BE ATTACHED TO THE SERVICE EQUIPMENT WITH POP-RIVOTS, SCREWS, OR EPOXY.

## Building

Wind Turbine on Roof or

Show location if remote

From building

Emergency

Generator

Storage Batteries

in Garage/room 123

Solar Photovoltaic

on Roof